## Slide 1: 4G/5G Cell Traffic KPI Forecasting based on Dense-MLP
2021-11-30
Digi Pioneer
ITU-T AI/ML in 5G challenge

## Slide 2
Background
4G/5G cell traffic KPI forecasting is a fundamental function of the network full life cycle.
More than 20% of intelligent network operation functions depend on cell traffic forecasting.
NETWORK
PLANNING
NETWORK
O & M
NETWORK
CONSTRUCTION
NETWORK
OPERATION
NETWORK
OPTIMIZATION
4G/5G Cell Traffic KPI
Forecasting Model

## Slide 3
Training data include hourly 4G/5G cell indicator data of 4 cities in a province in recent 6 months
Cell parameter data, including the base station name, cell name, coverage type, antenna information, bandwidth and some other information.
2×6 =12 indicators of 4G and 5G cells
Forecasting the indicators in 7-days and 1-hour frequency
Problem Statement
Forecast target
Training data
191GB original data for 4G cells
25GB original data for 5G cells
Challenge
Large Data
50GB storage, 32GB ram, Tesla v100GPU
Not very sufficient for data of 67,000 cells ×6 indicators ×2 standards
Limited Hardware
Resources
The score is a weighted average of MAPE error of each prediction
MAPE is sensitive to error when the true value is small
Sensitive scoring rules
Task Analysis
Challenges in this competition also reflect challenges in real network applications.

## Slide 4
Time series forecasting Algorithm
Use Cases in ITU AI Standards
Related Works
Prophet
LSTNet
Informer
Taylor S J , Letham B . Forecasting at Scale[J]. The American Statistician, 2018, 72.
Lai G, Chang W C, Yang Y, et al. Modeling long-and short-term temporal patterns with deep neural networks[C]//The 41st International ACM SIGIR Conference on Research & Development in Information Retrieval. 2018: 95-104.
Zhou H , Zhang S , Peng J , et al. Informer: Beyond Efficient Transformer for Long Sequence Time-Series Forecasting[J]. 2020.
ITU has specified some network intelligence use cases of cell traffic forecasting.
Researchers have proposed many classical time series forecasting algorithms for such cases.

## Slide 5
Original Data
(200+ GB in total)
Time Series Data
Neural Network Training Data
×12
(2 networks × 6 KPIs)
Neural Network Models
×12
Forecasting Input Data
Forecasting Result
Input
Hidden Layers
Output
Solution Overview

## Slide 6
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27
指标得分 | 1.0286 | 1.0246 | 0.7044 | 0.5516 | 0.4079 | 0.3739 | 0.3475 | 0.347 | 0.3425 | 0.3399 | 0.5 | 0.53 | 0.3294 | 0.3018 | 0.3024 | 0.3024 | 0.3025 | 0.3024 | 0.3024 | 0.3025 | 0.22 | 0.218 | 0.25 | 0.218 | 0.218 | 0.165 | 0.165 | 0.155 | 0.155 | 0.145 | 0.132
1.0286
0.5516
0.7597
0.28
0.2614
0.2484
2021-09-30
2021-07-27
Dynamic
learning
rate
Compositional
loss function
LSTM, ARIMA,
etc.
Dense-MLP
Rule-based
Historical data
Research Roadmap

## Slide 7
Data Insight:
The values during the Spring Festival look different; The data contains obvious daily and weekly seasonality.
Data Preprocessing:
Take only data after March 1, fill the null and zero with weighted average of the index values at the same relative time in several weeks before and after.
Data Insight & preprocessing

## Slide 8
Input
Hidden 1
Hidden 2
output
FC
FC
FC
FC
FC
FC
Additional fully-connected layers added
Reduce information loss of the feed forward process
Large parameter amount to fit data from 67k cells
Input: 3 weeks of historical data + holiday information of 4 weeks (3 week history + 1 week predicted)
Output: 1 week of future data
Utilizes holiday data for better prediction
Solution(1): Dense-MLP Model structure

## Slide 9
12 models trained in total:
1 model for each 4G indicator, trained on about 1.9 million rows of preprocessed data.
1 model for each 5G indicator, based on the corresponding 4G model and incrementally trained on bout 0.13 million rows of preprocessed data.
Parameters to ensure fast convergence:
Linearly decreasing learning rate with different batch size tuned for different indicators
~4 hours training time on single T100 GPU
Customized loss function to minimize MAPE loss：
Unified Absolute Error (UAE) : Divide APE by mean of each row of real value.
Solution(2): Optimizations for Training Process
利用拨测系统对故障点进行拨测的最
终确认
主动验证

## Slide 10
Accurate Prediction
Fast Training & Inference
4 hours training time for processed KPI data of 67000 cells
10 minutes inference time for top 20% cells
Flexible Deployment
Adaptable to any scenario with different network scale and computing ability with various AI platforms.
Major Advantages
Using the historical 4G/5G cell traffic data of 4 cities in the past 6 months, the prediction error (MAPE) of hourly cell traffic KPI shown by the model for the next 7 days is only 0.2484.
Properly fitting the training data and not overfitting.

## Slide 11
Final score：0.2484, 1st prize
Achievement(1): the competition
1st prize

## Slide 12
Achievement(2): Application
NR
LTE
EPC
Sunset Model
Network energy efficiency modeling
4G/5G Cell Traffic KPI
Prediction Model
…
Network energy efficiency evaluation system
Energy efficiency model of network equipments
Network energy efficiency modeling
5G Energy-saving Operation
Energy-saving Scheme Generation
Cell Value
PrbAssnRate
Cell Perfomance
WirelessSuccConnRate
UE Service Types
Number of VIP UE
Cell Basic Information
electricity fees
Rental cost
AvgDataRate
MOS
coverage scenario
The model has been integrated into our network energy-saving system and applied on 5G network of JiangSu Province, China .Our proposal for M.resm-AI has been approved by ITU.
Energy saving for different type of base station

## Slide 13
The 4G/5G cell traffic KPI forecast model will be widely applied on intelligent 5g network operation and maintenance products.
Custmer Experience Management
Network Qualify Evaluation
Cell Coverage Optimization
Radio Resource Management
Achievement(3): More Applications
4G/5G Cell Traffic KPI Forecast Model

## Slide 14
Optimize the network architecture on real data with commonly-used network components such as convolutions, recursive layers, dilated convolutions or Transformer-like structures.
Perform Space-Time forecasting with spatial information of cells.
Outlook
Zhou H , Zhang S , Peng J , et al. Informer: Beyond Efficient Transformer for Long Sequence Time-Series Forecasting[J]. 2020.
Wu Z , Pan S , Chen F , et al. A Comprehensive Survey on Graph Neural Networks[J]. IEEE Transactions on Neural Networks and Learning Systems, 2019.

## Slide 15
Thank you